## Slide 1: Computer Arithmetic
國立清華大學資訊工程學系
黃婷婷教授

## Slide 2: Outline
Addition and subtraction
Constructing an arithmetic logic unit
  Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry look-ahead adder
    Multiple level carry look-ahead adder
Multiplication
  Unsigned multiply
  Signed multiply
Division
Floating point
  Representations
  Addition and multiplication

## Slide 3: Outline
Addition and subtraction
Constructing an arithmetic logic unit
  Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry look-ahead adder
    Multiple level carry look-ahead adder
Multiplication
  Unsigned multiply
  Signed multiply
Division
Floating point
  Representations
  Addition and multiplication

## Slide 4: Problem: Designing MIPS ALU
Requirements: must support the following arithmetic and logic operations
  add, sub: two’s complement adder/subtractor with overflow detection
  and, or, nor : logical AND, logical OR, logical NOR
  slt (set on less than): two’s complement adder with inverter, check sign bit of result

## Slide 5: Functional Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 6: Functional Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
5
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 7: A Bit-slice ALU
ALU31
a31
b31
m
cin
c31
s31
A
B
ALUop
Result
32
32
32
4
Overflow
ALU0
a0
b0
m
cin
co
s0
Zero
Design trick 1: divide and conquer
  Break the problem into simpler problems, solve them and glue together the solution
Design trick 2: solve part of the problem and extend

## Slide 8: A 1-bit ALU
A
B
1-bit
Full
Adder
CarryOut
Mux
CarryIn
Result
add
and
or
Operation
Design trick 3: take pieces you know (or can imagine) and try to put them together
0
1
2
Notes: Now that I have shown you how to build a 1-bit full adder, we have all the major components needed for this 1-bit ALU.
In order to build a 4-bit ALU, we simply connect four 1-bit ALUs in series to feed the CarryOut of one ALU to the CarryIn of the next ALU.
Even though I called this an ALU, I actually lied a little. There is something missing about this ALU. This ALU can NOT perform the subtract operation.
Let see how can we fix this problem.
2 min = 35 min. (Y:15)

## Slide 9: Functional Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
8
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 10: A 4-bit ALU
1-bit ALU 4-bit ALU
A
B
1-bit
Full
Adder
CarryOut
Mux
CarryIn
Result
A0
B0
1-bit
ALU
Result0
CarryIn0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
CarryOut2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
Operation
Operation
Notes: Now that I have shown you how to build a 1-bit full adder, we have all the major components needed for this 1-bit ALU.
In order to build a 4-bit ALU, we simply connect four 1-bit ALUs in series to feed the CarryOut of one ALU to the CarryIn of the next ALU.
Even though I called this an ALU, I actually lied a little. There is something missing about this ALU. This ALU can NOT perform the subtract operation.
Let see how can we fix this problem.
2 min = 35 min. (Y:15)

## Slide 11: How about Subtraction?
ALU
A
B’
Result
CarryIn
CarryOut
B
0
1
Mux
Sel
Subtract
(Bnegate)
2’s complement: take inverse of every bit and add 1 (at cin of first stage)
  A + B’ + 1 = A + (B’ + 1) = A + (-B) = A - B
  Bit-wise inverse of B is B’
Operation
Notes: Recalled something you learned from grade school that: A - B is the same as A plus (-B).
Also recall from earlier slides that in order to calculate the 2 complement representation of negative B, we simply take the inverse of very bit and add 1.
The bitwise inverse of B is easy to compute. Just pass them through the inverter.
In order to do the add 1 operation, we simply set the CarryIn to 1.
So for the subtract operation, we simply select the output of the inverter and set CarryIn to 1.
Then we will be adding A to the negative of B and whola, we have the A minus B operation.
+2 = 37 min. (Y:17)

## Slide 12: Revised Diagram
A
B
ALUop
Result
32
32
32
4
Overflow
ALU0
a0
b0
cin
co
s0
ALU31
a31
b31
cin
c31
s31
Supply a 1 on subtraction
?
Zero
LSB and MSB need to do a little extra
Combining the CarryIn and Bnegate

## Slide 13: Functional Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 14: R-Format Instructions (1/2)
6
5
5
5
6
5
opcode
rs
rt
rd
funct
shamt
Define the following “fields”:
  opcode: partially specifies what instruction it is (Note: 0 for all R-Format instructions)
  funct: combined with opcode to specify the instruction
  Question: Why aren’t opcode and funct a single 12-bit field?
  rs (Source Register): generally used to specify register containing first operand
  rt (Target Register): generally used to specify register containing second operand
  rd (Destination Register): generally used to specify register which will receive result of computation

## Slide 15: Nor Operation
0
Operation
1
0
1
b
2
ALUop
A nor B = (not A) and (not B)
Result
CarryOut
Ainvert
CarryIn
0
1
a
Bnegate
2

## Slide 16: Functional Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 17: Outline
Addition and subtraction
Constructing an arithmetic logic unit
  Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry look-ahead adder
    Multiple level carry look-ahead adder
Multiplication
  Unsigned multiply
  Signed multiply
Division
Floating point
  Representations
  Addition and multiplication
16

## Slide 18: Functional Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 19: Set on Less Than (I)
0
3
Operation
1
0
1
b
2
ALUop
1-bit in ALU
(for bits 1-30)
Less
(0:bits 1-30)
Result
CarryOut
Ainvert
CarryIn
0
1
a
Bnegate

## Slide 20: Set on Less Than (II)
Overflow
detection
0
3
Operation
a
1
0
1
b
2
Sign bit in ALU
Less
Result
Ainvert
CarryIn
Set
Overflow
Bnegate
0
1

## Slide 21: Set on Less Than (III)
0
3
Operation
1
0
1
b
2
ALUop
Bit 0 in ALU
Set
Result
CarryOut
Ainvert
CarryIn
0
1
a
Bnegate

## Slide 22: A Ripple Carry Adder and Set on Less Than
ALUop Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-less-than
  1100 nor

## Slide 23: Functional Specification
ALU Control (ALUop) Function
  0000 and
  0001 or
  0010 add
  0110 subtract
  0111 set-on-less-than
  1100 nor
ALU
32
32
32
A
B
Result
Overflow
Zero
4
ALUop
CarryOut
22
Notes: Now you remember what binary numbers are, let design an Arithmetic Logic Unit that can perform bitwise AND, bitwise OR, binary add, binary subtract, and et-on-less-than.
The type of operation the ALU perform will be selected by the ALUop bits.
The ALU I am going to show you in class is 4 bits wide (N = 4). The ALU you need to design for the next homework assignment will be 32 bits wide.
I will show you how to implement all these operations except the last one, which is left as your homework assignment.
+1 = 25 min. (Y:05)

## Slide 24: Overflow
Decimal Binary Decimal 2’s complement
0 0000 0 0000
1 0001 -1 1111
2 0010 -2 1110
3 0011 -3 1101
4 0100 -4 1100
5 0101 -5 1011
6 0110 -6 1010
7 0111 -7 1001
-8 1000
Ex: 7 + 3 = 10 but ... - 4 - 5 = - 9 but …
0 1 1 1 1 0 0 0
0 1 1 1 7 1 1 0 0 -4
+ 0 0 1 1 3 + 1 0 1 1 -5
1 0 1 0 -6 0 1 1 1 7

## Slide 25: Overflow Detection
Overflow: result too big/small to represent
  -8  4-bit binary number  7
  When adding operands with different signs, overflow cannot occur!
  Overflow occurs when adding:
    2 positive numbers and the sum is negative
    2 negative numbers and the sum is positive
    => sign bit is set with the value of the result
  Overflow if: Carry into MSB  Carry out of MSB
0 1 1 1 1 0 0 0
0 1 1 1 7 1 1 0 0 -4
+ 0 0 1 1 3 + 1 0 1 1 -5
1 0 1 0 -6 0 1 1 1 7
Notes: Recalled from some earlier slides that the biggest positive number you can represent using 4-bit is 7 and the smallest negative you can represent is negative 8.
So any time your addition results in a number bigger than 7 or less than negative 8, you have an overflow.
Keep in mind is that whenever you try to add two numbers together that have different signs, that is adding a negative number to a positive number, overflow can NOT occur.
Overflow occurs when you to add two positive numbers together and the sum has a negative sign. Or, when you try to add negative numbers together and the sum has a positive sign.
If you spend some time, you can convince yourself that If the Carry into the most significant bit is NOT the same as the Carry coming out of the MSB, you have a overflow.
+2 = 41 min. (Y:21)

## Slide 26: Overflow Detection Logic
A0
B0
1-bit
ALU
Result0
CarryIn0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
Overflow
X
Y
X XOR Y
0
0
0
0
1
1
1
0
1
1
1
0
Overflow = CarryIn[N-1] XOR CarryOut[N-1]
Notes: Recall the XOR gate implements the not equal function: that is, its output is 1 only if the inputs have different values.
Therefore all we need to do is connect the carry into the most significant bit and the carry out of the most significant bit to the XOR gate.
Then the output of the XOR gate will give us the Overflow signal.
+1 = 42 min. (Y:22)

## Slide 27: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions
  On overflow, invoke exception handler
    Save PC in exception program counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from coprocessor reg) instruction can retrieve (copy) EPC value (to a general purpose register), to return after corrective action (by jump register instruction)

## Slide 28: Zero Detection Logic
CarryIn0
A0
B0
1-bit
ALU
Result0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
CarryOut2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
Zero
Zero Detection Logic is a one BIG NOR gate (support conditional jump)
Notes: Besides detecting overflow, our ALU also needs to indicate if the result is zero.
This is easy to do. All we need is a BIG NOR gate.
Then if any of the Result bit is not zero, then the output of the NOR gate will be low.
The only time the output of the NOR gate is high is when all the result bits are zeroes.
+1 = 43 min. (Y:23)

## Slide 29: Problems with Ripple Carry Adder
A0
B0
1-bit
ALU
Result0
CarryOut0
A1
B1
1-bit
ALU
Result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
Result2
CarryIn2
A3
B3
1-bit
ALU
Result3
CarryIn3
CarryOut3
CarryOut2
CarryIn0
CarryIn
CarryOut
A
B
Design Trick: look for parallelism and throw hardware at it
Carry bit may have to propagate from LSB to MSB => worst case delay: N-stage delay
28
Notes: The Adder we just built is called a Ripple Carry Adder because: Carry may have to propagate from the least significant bit to the most significant bit.
In other words, the combination of A0, B0, and CarryIn0 may cause CarryOut0 to become 1.
As a result of CarryOut0 going 1, CarryOut1 may become 1 and etc., etc., .... etc and propagate down the carry chain.
Recall the Carry Logic: CarryIn to CarryOut has a 2-gate delay.
So in the worst case, a N-bit ripple carry will have a 2N gate delay.
For a 32-bit adder, this means the worst case delay is 64 gates. This can be a problem.
So after the break, I will show you some faster way of designing an ALU.
+2 = 45 min. (Y:25)

## Slide 30: Outline
Addition and subtraction
Constructing an arithmetic logic unit
  Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry look-ahead adder
    Multiple level carry look-ahead adder
Multiplication
  Unsigned multiply
  Signed multiply
Division
Floating point
  Representations
  Addition and multiplication
29

## Slide 31: Carry Look-ahead: Theory (I) (Appendix C)
CarryOut=(B*CarryIn)+(A*CarryIn)+(A*B)
  Cin1=Cout0= (B0 * Cin0)+(A0 * Cin0)+ (A0 * B0)
  Cin2=Cout1= (B1 * Cin1)+(A1 * Cin1)+ (A1 * B1)
Substituting Cin1 into Cin2:
  Cin2=(A1*A0*B0)+(A1*A0*Cin0)+(A1*B0*Cin0) +(B1*A0*B0)+(B1*A0*Cin0)+(B1*B0*Cin0) +(A1*B1)
A0
B0
1-bit
ALU
Cout0
A1
B1
1-bit
ALU
Cin1
Cout1
Cin2
Cin0
Notes: Carry lookahead is another way to speed up an adder and here is the theory behind it.
Remember the logic equation for CarryOut so the carry coming out of bit 1 and into bit 2 (Cin2) looks like this.
Notice that, this carry will depends on the carry coming out of bit 0 (Cin1).
By substituting the equation of Cin1 into the equation Cin2, we can rewrite the equation of Cin2 so it depends on Cin0, A0, B0, A1, and B1.
The beauty of this equation is that it does NOT depend of the carry coming out of bit 0 (Cout0) so it does not have to wait for the carry to propagate through the lower bits.
This equation can be simplified if we redefine two terms: carry generate and propagate.
+2 = 55 min. (Y:35)

## Slide 32: Carry Look-ahead: Theory (II)
Now define two new terms:
  Generate Carry at Bit i: gi = Ai * Bi
  Propagate Carry via Bit i: pi = Ai xor Bi
We can rewrite:
  Cin1=g0+(p0*Cin0)
  Cin2=g1+(p1*g0)+(p1*p0*Cin0)
  Cin3=g2+(p2*g1)+(p2*p1*g0)+(p2*p1*p0*Cin0)
Carry going into bit 3 is 1 if
  We generate a carry at bit 2 (g2)
  Or we generate a carry at bit 1 (g1) and bit 2 allows it to propagate (p2 * g1)
  Or we generate a carry at bit 0 (g0) and bit 1 as well as bit 2 allows it to propagate …..
Notes: Using the carry generate and carry propagate terms, we can rewrite the carry lookahead equations like these.
For example, the Carry going into bit 3 (Cin 3) is 1 if:
(a) We generate a carry at bit 2.
(b) Or we generate a carry at bit 1 and bit 2 allows it to propagate ... and so on.
+1 = 56 min. (Y:36)

## Slide 33: A Plumbing Analogy for Carry Loo-kahead (1, 2, 4 bits)
Notes: Using the carry generate and carry propagate terms, we can rewrite the carry lookahead equations like these.
For example, the Carry going into bit 3 (Cin 3) is 1 if:
(a) We generate a carry at bit 2.
(b) Or we generate a carry at bit 1 and bit 2 allows it to propagate ... and so on.
+1 = 56 min. (Y:36)

## Slide 34: Common Carry Look-ahead Adder
Expensive to build a “full” carry look-ahead adder
  Ex: Cin3=g2+(p2*g1)+(p2*p1*g0)+(p2*p1*p0*Cin0)
  Just imagine length of the equation for Cin31
Common practices:
  Cascaded carry look-ahead adder
  Multiple level carry look-ahead adder
Notes: As you can imagine from looking at the carry lookahead equations, it is very expensive if you want to build a full 32-bit carry lookahead adder: the equation for Cin31 will be very long.
A common practice is to build smaller N-bit carry lookahead adders and then connect them together to form a bigger adder.
For example, here we connect four 8-bit carry lookahead adders to form a 32-bit adder.
+1 = 57 min. (Y:37)

## Slide 35: Cascaded Carry Look-ahead
8-bit Carry
Lookahead
Adder
C0
8
8
8
Result[7:0]
B[7:0]
A[7:0]
8-bit Carry
Lookahead
Adder
C8
8
8
8
Result[15:8]
B[15:8]
A[15:8]
8-bit Carry
Lookahead
Adder
C16
8
8
8
Result[23:16]
B[23:16]
A[23:16]
8-bit Carry
Lookahead
Adder
C24
8
8
8
Result[31:24]
B[31:24]
A[31:24]
Connects several N-bit look-ahead adders to form a big one
Notes: As you can imagine from looking at the carry lookahead equations, it is very expensive if you want to build a full 32-bit carry lookahead adder: the equation for Cin31 will be very long.
A common practice is to build smaller N-bit carry lookahead adders and then connect them together to form a bigger adder.
For example, here we connect four 8-bit carry lookahead adders to form a 32-bit adder.
+1 = 57 min. (Y:37)

## Slide 36: Example: Carry Look-ahead Unit
Carry Look-ahead Unit
pi
4
cin
cout
4
gi
4

## Slide 37: Example: Cascaded Carry Look-ahead
Connects several N-bit look-ahead adders to form a big one
4-bit Carry
Lookahead
Unit
4-bit Carry
Lookahead
Unit
4-bit Carry
Lookahead
Unit
4-bit Carry
Lookahead
Unit
c0
g[3:0]
p[3:0]
c4
g[7:4]
p[7:4]
c8
g[11:8]
p[11:8]
c12
c[4:1]
g[15:12]
p[15:12]
c[8:5]
c[12:9]
c[16:13]
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Notes: As you can imagine from looking at the carry lookahead equations, it is very expensive if you want to build a full 32-bit carry lookahead adder: the equation for Cin31 will be very long.
A common practice is to build smaller N-bit carry lookahead adders and then connect them together to form a bigger adder.
For example, here we connect four 8-bit carry lookahead adders to form a 32-bit adder.
+1 = 57 min. (Y:37)

## Slide 38: Outline
Addition and subtraction
Constructing an arithmetic logic unit
  Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry look-ahead adder
    Multiple level carry look-ahead adder
Multiplication
  Unsigned multiply
  Signed multiply
Division
Floating point
  Representations
  Addition and multiplication
37

## Slide 39: Multiple Level Carry Look-ahead Adder
View an N-bit look-ahead adder as a block
Where to get Cin of the block ?
  Generate “super” Pi and Gi of the block
  Use next level carry look-ahead structure to generate block Cin
8-bit Carry
Lookahead
Adder
C0
8
8
8
Result[7:0]
B[7:0]
A[7:0]
8-bit Carry
Lookahead
Adder
C8
8
8
8
Result[15:8]
B[15:8]
A[15:8]
8-bit Carry
Lookahead
Adder
C16
8
8
8
Result[23:16]
B[23:16]
A[23:16]
8-bit Carry
Lookahead
Adder
C24
8
8
8
Result[31:24]
B[31:24]
A[31:24]
Notes: As you can imagine from looking at the carry lookahead equations, it is very expensive if you want to build a full 32-bit carry lookahead adder: the equation for Cin31 will be very long.
A common practice is to build smaller N-bit carry lookahead adders and then connect them together to form a bigger adder.
For example, here we connect four 8-bit carry lookahead adders to form a 32-bit adder.
+1 = 57 min. (Y:37)

## Slide 40: A Plumbing Analogy for Carry Look-ahead (Next Level P0 and G0)
Notes: Using the carry generate and carry propagate terms, we can rewrite the carry lookahead equations like these.
For example, the Carry going into bit 3 (Cin 3) is 1 if:
(a) We generate a carry at bit 2.
(b) Or we generate a carry at bit 1 and bit 2 allows it to propagate ... and so on.
+1 = 56 min. (Y:36)

## Slide 41: A Carry Look-ahead Adder
A B Cout
0 0 0 kill
0 1 Cin propagate
1 0 Cin propagate
1 1 1 generate
G = A * B
P = A + B
Notes: Names: suppose G0 is 1 => carry no matter what else => generates a carry
suppose G0 =0 and P0=1 => carry IFF C0 is a 1 => propagates a carry
Like dominoes
What about more than 4 bits?

## Slide 42: Example: Carry Look-ahead Unit
Carry Look-ahead Unit
pi
4
cin
cout
4
gi
4
P
G

## Slide 43: Example: Multiple Level Carry Look-ahead
4-bit Carry
Lookahead
Unit
4-bit Carry
Lookahead
Unit
4-bit Carry
Lookahead
Unit
4-bit Carry
Lookahead
Unit
c0
g[3:0]
p[3:0]
c4
g[7:4]
p[7:4]
c8
g[11:8]
p[11:8]
c12
c[4:1]
g[15:12]
p[15:12]
c[8:5]
c[12:9]
c[16:13]
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
4-bit Carry
Lookahead
Unit
P3, G3
P2, G2
P1, G1
P0, G0
C[4:0]
+

## Slide 44: Carry-select Adder
n-bit adder
n-bit adder
CP(2n) = 2*CP(n)
n-bit adder
n-bit adder
n-bit adder
1
0
Cout
CP(2n) = CP(n) + CP(mux)
Design trick: guess
Notes: Use multiplexor to save time: guess both ways and then select
(assumes mux is faster than adder)

## Slide 45: Arithmetic for Multimedia
Graphics and media processing operates on vectors of 8-bit and 16-bit data
  Use 64-bit adder, with partitioned carry chain
    Operate on 8×8-bit, 4×16-bit, or 2×32-bit vectors
  SIMD (single-instruction, multiple-data)
Saturating operations
  On overflow, result is largest representable value
    c.f. 2s-complement modulo arithmetic
  E.g., clipping in audio, saturation in video

## Slide 46: Outline
Addition and subtraction
Constructing an arithmetic logic unit
  Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry look-ahead adder
    Multiple level carry look-ahead adder
Multiplication
  Unsigned multiply
  Signed multiply
Division
Floating point
  Representations
  Addition and multiplication
45

## Slide 47: Outline
Addition and subtraction
Constructing an arithmetic logic unit
  Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry look-ahead adder
    Multiple level carry look-ahead adder
Multiplication
  Unsigned multiply
  Signed multiply
Division
Floating point
  Representations
  Addition and multiplication
46

## Slide 48: MIPS R2000 Organization

## Slide 49: Multiplication in MIPS
mult $t1, $t2 # t1 * t2
No destination register: product could be ~264; need two special registers to hold it
3-step process:
00011111111111111111111111111111 11000000000000000000000000000000
Hi Lo
01000000000000000000000000000000
X $t2
01111111111111111111111111111111
$t1
00011111111111111111111111111111
$t3
11000000000000000000000000000000
$t4
mflo $t4
mfhi $t3
Notes: Don’t have to understand the multiplication process YET. MUST UNDERSTAND that HI ORDER BITS in HI, LOW ORDER BITS in LO, (noise) MUST USE MFHI, MFLO to access.

## Slide 50: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd

## Slide 51: Unsigned Multiply
Paper and pencil example (unsigned):
Multiplicand 1000ten Multiplier X 1001ten 1000
0000 0000 1000 Product 01001000ten
m bits x n bits = m+n bit product
Binary makes it easy:
  0 => place 0 ( 0 x multiplicand)
  1 => place a copy ( 1 x multiplicand)
2 versions of multiply hardware and algorithm

## Slide 52: Unsigned Multiplier (Ver. 1)
64-bit multiplicand register (with 32-bit multiplicand at right half), 64-bit ALU, 64-bit product register, 32-bit multiplier register

## Slide 53: Multiply Algorithm (Ver. 1)
3. Shift Multiplier register right 1 bit
2. Shift Multiplicand register left 1 bit
0010 x 0011
Product Multiplier Multiplicand
0000 0000 0011 0000 0010
0000 0010 0001 0000 0100
0000 0110 0000 0000 1000
0000 0110 0000 0001 0000
0000 0110 0000 0010 0000
Done
Yes: 32 repetitions
No: < 32 repetitions
1. Test
Multiplier0
Multiplier0 = 0
Multiplier0 = 1
1a. Add multiplicand to product and
place the result in Product register
32nd
repetition?
Start
Notes: Mer: 0011 Mnd: 0000 0010 P: 0000 0000
1a. 1=>P=P+Mcand Mer: 0011 Mcand: 0000 0010 P: 0000 0010
2. Shl Mcand Mer: 0011 Mcand: 0000 0100 P: 0000 0010
3. Shr Mer Mer: 0001 Mcand: 0000 0100 P: 0000 0010
1a. 1=>P=P+Mcand Mer: 0001 Mcand: 0000 0100 P: 0000 0110
2. Shl Mcand Mer: 0001 Mcand: 0000 1000 P: 0000 0110
3. Shr Mer Mer: 0000 Mcand: 0000 1000 P: 0000 0110
1. 0=>nop Mer: 0000 Mcand: 0000 1000 P: 0000 0110
2. Shl Mcand Mer: 0000 Mcand: 0001 0000 P: 0000 0110
3. Shr Mer Mer: 0000 Mcand: 0001 0000 P: 0000 0110
1. 0=>nop Mer: 0000 Mcand: 0001 0000 P: 0000 0110
2. Shl Mcand Mer: 0000 Mcand: 0010 0000 P: 0000 0110
3. Shr Mer Mer: 0000 Mcand: 0010 0000 P: 0000 0110

## Slide 54: Observations: Multiply Ver. 1
Delay ratio of multiply to add 5:1 to 100:1
Half of the bits in multiplicand always 0 => 64-bit adder is wasted
0’s inserted in right of multiplicand as shifted => least significant bits of product never changed once formed
Instead of shifting multiplicand to left, shift product to right?
Product register wastes space => combine Multiplier and Product register

## Slide 55: Unsigned Multiply
Paper and pencil example (unsigned):
Multiplicand 1000ten Multiplier X 1001ten 1000
0000 0000 1000 Product 01001000ten
m bits x n bits = m+n bit product
Binary makes it easy:
  0 => place 0 ( 0 x multiplicand)
  1 => place a copy ( 1 x multiplicand)
2 versions of multiply hardware and algorithm

## Slide 56: Unisigned Multiplier (Ver. 2)
32-bit Multiplicand register, 32 -bit ALU, 64-bit Product register (HI & LO in MIPS), (0-bit Multiplier register)

## Slide 57: Multiply Algorithm (Ver. 2)
32nd
repetition?
2. Shift Product register right 1 bit
1a. Add multiplicand to left half of product and
place the result in left half of Product register
0010 x 0011
Multiplicand Product 0010 0000 0011
0010 0011
0010 0001 0001
0011 0001
0010 0001 1000
0010 0000 1100
0010 0000 0110
Done
Yes: 32 repetitions
No: < 32 repetitions
1. Test
Product0
Product0 = 0
Product0 = 1
Start
Notes: Mcand: 0010 P: 0000 0011
1a. 1=>P=P+Mcand Mcand: 0010 P: 0010 0011
2. Shr P Mcand: 0010 P: 0001 0001
1a. 1=>P=P+Mcand Mcand: 0010 P: 0011 0001
2. Shr P Mcand: 0010 P: 0001 1000
1. 0=>nop Mcand: 0010 P: 0001 1000
2. Shr P Mcand: 0010 P: 0000 1100
1. 0=>nop Mcand: 0010 P: 0000 1100
2. Shr P Mcand: 0010 P: 0000 0110

## Slide 58: Outline
Addition and subtraction
Constructing an arithmetic logic unit
  Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry look-ahead adder
    Multiple level carry look-ahead adder
Multiplication
  Unsigned multiply
  Signed multiply
Division
Floating point
  Representations
  Addition and multiplication
57

## Slide 59: Signed Multiply
What about signed multiplication?
  The easiest solution is to make both positive and remember whether to complement product when done (leave out sign bit, run for 31 steps)
  Apply definition of 2’s complement
    sign-extend partial products and subtract at end
58

## Slide 60: Using Definition of 2’s Complement
Paper and pencil example (signed):
Multiplicand 1001 (-7)
Multiplier X 1001 (-7) 11111001
+ 0000000 + 000000 - 11001 Product 00110001 (49)
Rule 1: Multiplicand sign extended
Rule 2: Sign bit (s) of Multiplier
  0 => 0 x multiplicand
  1 => -1 x multiplicand
Why rule 2 ?
  X = s xn-2 xn-3…. x1 x0 (2’s complement)
  Value(X) = - 1 x s x 2n-1 + xn-2 x 2n-2 +… + x1 x 21+ x0 x 20

## Slide 61
00100000
00000001
--------------------
00011111

## Slide 62: Booth’s Algorithm: Motivation
Example: 2 x 6 = 0010 x 0110: 0010two x 0110two + 0000 shift (0 in multiplier) + 0010 add (1 in multiplier) + 0010 add (1 in multiplier) + 0000 shift (0 in multiplier) 0001100two
Can get same result in more than one way: 6 = -2 + 8 0110 = -00010 + 01000
Basic idea: replace a string of 1s with an initial subtract on seeing a one and add after last one 0010two x 0110two 0000 shift (0 in multiplier) - 0010 sub (first 1 in multiplier) 0000 shift (mid string of 1s) + 0010 add (prior step had last 1) 00001100two

## Slide 63: Booth’s Algorithm: Rationale
Current Bit to Explanation Example Op
bit right
1 0 Begins run of 1s 00001111000 sub
1 1 Middle run of 1s 00001111000 none
0 1 End of run of 1s 00001111000 add
0 0 Middle run of 0s 00001111000 none
Originally for speed (when shift was faster than add)
Why it works?
0 1 1 1 1 0
beginning of run
end of run
middle of run
-1
+ 10000
01111

## Slide 64: Booth’s Algorithm
1. Depending on the current and previous bits, do one of the following: 00: Middle of a string of 0s, no arithmetic op. 01: End of a string of 1s, so add multiplicand to the left half of the product 10: Beginning of a string of 1s, so subtract multiplicand from the left half of the product 11: Middle of a string of 1s, so no arithmetic op.
2. As in the previous algorithm, shift the Product register right (arithmetically) 1 bit
Notes: 0. 0010 x 0000 0110 0
1a. 00 nop: 0000 0110 0
2. Shr: 0000 0011 0 (2 x 3)
1c: 10 Pr-M 1110 0011 0
2. Shr: 1111 0001 1
1d. 11 nop 1111 0001 1
2. Shr: 1111 1000 1
1b: 01 PR+M 0001 1000 1
2. Shr: 0000 1100 0
0. 0010 x 0000 1101 0 (2 x -3)
1c: 10 Pr-M : 1110 1101 0
2. Shr: 1111 0110 1
1b: 01 PR+M 0001 0110 1
2. Shr: 0000 1011 0
1c: 10 Pr-M : 1110 1011 0
2. Shr: 1111 0101 1
1d. 11 nop 1111 0101 1
2. Shr: 1111 1010 1

## Slide 65: Booths Example (2 x 7)
Operation Multiplicand Product next?
0. initial value 0010 0000 0111 0 10 -> sub
1a. P = P - m 1110 +1110
1110 0111 0 shift P (sign ext)
1b. 0010 1111 0011 1 11 -> nop, shift
2. 0010 1111 1001 1 11 -> nop, shift
3. 0010 1111 1100 1 01 -> add
4a. 0010 +0010
0001 1100 1 shift
4b. 0010 0000 1110 0 done

## Slide 66: Booths Example (2 x -3)
Operation Multiplicand Product next?
0. initial value 0010 0000 1101 0 10 -> sub
1a. P = P - m 1110 +1110
1110 1101 0 shift P (sign ext)
1b. 0010 1111 0110 1 01 -> add
0010 +0010
2a. 0001 0110 1 shift P
2b. 0010 0000 1011 0 10 -> sub
1110 +1110
3a. 0010 1110 1011 0 shift
3b. 0010 1111 0101 1 11 -> nop
4a 1111 0101 1 shift
4b. 0010 1111 1010 1 done

## Slide 67: Faster Multiplier
A combinational multiplier
Use multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 68: Wallace Tree Multiplier
Use carry save adders: three inputs and two outputs
1 0 1 0 1 1 1 0
0 0 1 0 0 0 1 1
1 0 0 0 0 1 1 1
----------------
0 0 0 0 1 0 1 0 (sum)
1 0 1 0 0 1 1 1 (carry)
8 full adders
One full adder delay (no carry propagation)
The last stage is performed by regular adder
What is the minimum delay for 16 x 16 multiplier ?

## Slide 69: 8-bit Wallace Tree Multiplier
CSA
CSA
CSA
CSA
CSA
CSA
Regular adder
M0
M1
M2
M3
M4
M5
M6
M7

## Slide 70: Outline
Addition and subtraction (Sec. 3.2)
Constructing an arithmetic logic unit (Appendix C)
  Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry look-ahead adder
    Multiple level carry look-ahead adder
Multiplication (Sec. 3.3, Appendix C)
  Unsigned multiply
  Signed multiply
Division (Sec. 3.4)
Floating point (Sec. 3.5)
  Representations
  Addition and multiplication
69

## Slide 71: MIPS R2000 Organization

## Slide 72: Division in MIPS
div $t1, $t2 # t1 / t2
Quotient stored in Lo, remainder in Hi
mflo $t3 #copy quotient to t3
mfhi $t4 #copy remainder to t4
3-step process
Unsigned division:
divu $t1, $t2 # t1 / t2
  Just like div, except now interpret t1, t2 as unsigned integers instead of signed
  Answers are also unsigned, use mfhi, mflo to access
No overflow or divide-by-0 checking
  Software must perform checks if required

## Slide 73: Divide: Paper & Pencil
1001ten Quotient
Divisor 1000ten 1001010ten Dividend -1000 0010 0101 1010 -1000 10ten Remainder
See how big a number can be subtracted, creating quotient bit on each step
  Binary => 1 * divisor or 0 * divisor
Two versions of divide, successive refinement
Both dividend and divisor are 32-bit positive integers

## Slide 74: Divide Hardware (Version 1)
Remainder
Quotient
Divisor
64-bit ALU
Shift Right
Shift Left
Write
Control
32 bits
64 bits
64 bits
64-bit Divisor register (initialized with 32-bit divisor in left half), 64-bit ALU, 64-bit Remainder register (initialized with 64-bit dividend), 32-bit Quotient register

## Slide 75: Divide Algorithm (Version 1)
3. Shift Divisor register right 1 bit
No: < 33 repetitions
2b. Restore original value by adding Divisor to Remainder, place sum in Remainder, shift Quotient to the left, setting new least significant bit to 0
Test Remainder
Remainder < 0
Remainder  0
1. Subtract Divisor register from
Remainder register, and place the
result in Remainder register
2a. Shift Quotient register to left, setting new rightmost bit to 1
Done
Yes: 33 repetitions
Start: Place Dividend in Remainder
33rd
repetition?
0111 / 0010
Quot. Divisor Rem.
0000 00100000 00000111 11100111 00000111 0000 00010000 00000111 11110111 00000111 0000 00001000 00000111 11111111 00000111 0000 00000100 00000111 00000011 0001 00000011 0001 00000010 00000011 00000001 0011 00000001 0011 00000001 00000001
Notes: Q: 0000 D: 0010 0000 R: 0000 0111  = 1110 0000
1: R = R Q: 0000 D: 0010 0000 R: 1110 0111
2b: +D, sl Q, 0 Q: 0000 D: 0010 0000 R: 0000 0111
3: Shr D Q: 0000 D: 0001 0000 R: 0000 0111  = 1111 0000
1: R = R Q: 0000 D: 0001 0000 R: 1111 0111
2b: +D, sl Q, 0 Q: 0000 D: 0001 0000 R: 0000 0111
3: Shr D Q: 0000 D: 0000 1000 R: 0000 0111  = 1111 1000
1: R = R Q: 0000 D: 0000 1000 R: 1111 1111
2b: +D, sl Q, 0 Q: 0000 D: 0000 1000 R: 0000 0111
3: Shr D Q: 0000 D: 0000 0100 R: 0000 0111  = 1111 1100
1: R = R Q: 0000 D: 0000 0100 R: 0000 0011
2a: sl Q, 1 Q: 0001 D: 0000 0100 R: 0000 0011
3: Shr D Q: 0000 D: 0000 0010 R: 0000 0011  = 1111 1110
1: R = R Q: 0000 D: 0000 0010 R: 0000 0001
2a: sl Q, 1 Q: 0011 D: 0000 0010 R: 0000 0001
3: Shr D Q: 0011 D: 0000 0001 R: 0000 0001
Recommend show 2 comp of divisor, show lines for subtract divisor and restore remainder

## Slide 76: Observations: Divide Version 1
Half of the bits in divisor register always 0 => 1/2 of 64-bit adder is wasted => 1/2 of divisor is wasted
Instead of shifting divisor to right, shift remainder to left?
1st step cannot produce a 1 in quotient bit => switch order to shift first and then subtract => save 1 iteration
Eliminate Quotient register by combining with Remainder register as shifted left

## Slide 77: Divide Hardware (Version 2)
Remainder
(Quotient)
Divisor
32-bit ALU
Write
Control
32 bits
64 bits
Shift Left
32-bit Divisor register, 32 -bit ALU, 64-bit Remainder register, (0-bit Quotient register)

## Slide 78: Divide Algorithm (Version 2)
Test Remainder
No: < 32 repetitions
0111 / 0010
Step Remainder Div. 0 0000 0111 0010
1.1 0000 1110
1.2 1110 1110
1.3b 0001 1100
2.2 1111 1100
2.3b 0011 1000 3.2 0001 1000
3.3a 0011 0001
4.2 0001 0001
4.3a 0010 0011
0001 0011
3b. Restore original value by adding Divisor to left half of Remainder, and place sum in left half of Remainder. Also shift Remainder to left, setting the new least significant bit to 0
Remainder < 0
Remainder  0
2. Subtract Divisor register from the left half of Remainder register, and place the
result in the left half of Remainder register
3a. Shift Remainder to left, setting new rightmost bit to 1
1. Shift Remainder register left 1 bit
Done. Shift left half of Remainder right 1 bit
Yes: 32 repetitions
32nd
repetition?
Start: Place Dividend in Remainder
Divide Algorithm (Version 2)
Notes: D: 0010 R: 0000 0111
0: Shl R D: 0010 R: 0000 1110
1: R = R D: 0010 R: 1110 1110
2b: +D, sl R, 0 D: 0010 R: 0001 1100
1: R = R D: 0010 R: 1111 1100
2b: +D, sl R, 0 D: 0010 R: 0011 1000
1: R = R D: 0010 R: 0001 1000
2a: sl R, 1 D: 0010 R: 0011 0001
1: R = R D: 0010 R: 0001 0001
2a: sl R, 1 D: 0010 R: 0010 0011
Shr R(rh) D: 0010 R: 0001 0011

## Slide 79: Divide
Signed Divides:
  Remember signs, make positive, complement quotient and remainder if necessary
  Let Dividend and Remainder have same sign and negate Quotient if Divisor sign & Dividend sign disagree,
  e.g., -7 2 = -3, remainder = -1
  -7- 2 = 3, remainder = -1
  Satisfy Dividend =Quotient x Divisor + Remainder

## Slide 80: Observations: Multiply and Divide
Same hardware as multiply: just need ALU to add or subtract, and 64-bit register to shift left (multiply: shift right)
Hi and Lo registers in MIPS combine to act as 64-bit register for multiply and divide

## Slide 81: Multiply/Divide Hardware
Product/
Remainder
(Multiplier/
Quotient)
Multiplicand/
Divisor
32-bit ALU
Write
Control
32 bits
64 bits
Shift Left
Shift Right
32-bit Multiplicand/Divisor register, 32 -bit ALU, 64-bit Product/Remainder register, (0-bit Multiplier/Quotient register)

## Slide 82: Outline
Addition and subtraction
Constructing an arithmetic logic unit
Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry lookahead adder
    Multiple level carry lookahead adder
Multiplication
  Unsigned multiply
  Signed multiply
Division
Floating point
  Representations
  Addition and multiplication
81

## Slide 83: Floating-Point: Motivation
What can be represented in N bits?
Unsigned 0 to 2n - 1
2’s Complement -2n-1 to 2n-1- 1
1’s Complement -2n-1+1 to 2n-1
Excess M -M to 2n - M - 1
But, what about ...
  very large numbers? 9,349,398,989,787,762,244,859,087,678
  very small number? 0.0000000000000000000000045691
  rationals 2/3
  irrationals 2
  transcendentals e, 

## Slide 84: Scientific Notation: Binary
Computer arithmetic that supports it is called floating point, because the binary point is not fixed, as it is for integers
Normalized form: no leading 0s (exactly one digit to left of decimal point)
Alternatives to represent 1/1,000,000,000
  Normalized: 1.0 x 10-9
  Not normalized: 0.1 x 10-8, 10.0 x 10-10
1.0two x 2-1
radix (base)
“binary point”
Significand (Mantissa)
exponent

## Slide 85: FP Representation
Normal format: 1.xxxxxxxxxxtwo  2yyyytwo
Want to put it into multiple words: 32 bits for single-precision and 64 bits for double-precision
A simple single-precision representation:
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits
S represents sign Exponent represents y’s Significand represents x’s

## Slide 86: Double Precision Representation
Next multiple of word size (64 bits)
Double precision (vs. single precision)
  But primary advantage is greater accuracy due to larger significand
0
31
S
Exponent
30
20
19
Significand
1 bit
11 bits
20 bits
Significand (cont’d)
32 bits

## Slide 87: IEEE 754 Standard (1/4)
Regarding single precision, DP similar
Sign bit: 1 means negative 0 means positive
Significand:
  To pack more bits, leading 1 implicit for normalized numbers
  1 + 23 bits single, 1 + 52 bits double
  always true: 0 < Significand < 1 (for normalized numbers)
Note: 0 has no leading 1, so reserve exponent value 0 just for number 0

## Slide 88: IEEE 754 Standard (2/4)
0
1111 1111
000 0000 0000 0000 0000 0000
1/2
0
0000 0001
000 0000 0000 0000 0000 0000
2
Exponent:
  Need to represent positive and negative exponents
  Also want to compare FP numbers as if they were integers, to help in value comparisons
  If use 2’s complement to represent? e.g., 1.0 x 2-1 versus 1.0 x2+1 (1/2 versus 2)
  If we use integer comparison for these two words, we will conclude that 1/2 > 2!!!

## Slide 89: Biased (Excess) Notation
Biased 7
0000 -7
0001 -6
0010 -5
0011 -4
0100 -3
0101 -2
0110 -1
0111 0
1000 1
1001 2
1010 3
1011 4
1100 5
1101 6
1110 7
1111 8

## Slide 90: IEEE 754 Standard (3/4)
1/2
0
0111 1110
000 0000 0000 0000 0000 0000
0
1000 0000
000 0000 0000 0000 0000 0000
2
Instead, let notation 0000 0000 be most negative, and 1111 1111 most positive
Called biased notation, where bias is the number subtracted to get the real number
  IEEE 754 uses bias of 127 for single precision: Subtract 127 from Exponent field to get actual value for exponent
  1023 is bias for double precision

## Slide 91: IEEE 754 Standard (4/4)
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits
Summary (single precision):
(-1)S x (1.Significand) x 2(Exponent-127)
Double precision identical, except with exponent bias of 1023

## Slide 92: Example: FP to Decimal
0
0110 1000
101 0101 0100 0011 0100 0010
Sign: 0 => positive
Exponent:
  0110 1000two = 104ten
  Bias adjustment: 104 - 127 = -23
Significand:
  1+2-1+2-3 +2-5 +2-7 +2-9 +2-14 +2-15 +2-17 +2-22 = 1.0 + 0.666115
Represents: 1.666115ten2-23  1.986  10-7

## Slide 93: Example 1: Decimal to FP
1
0111 1110
100 0000 0000 0000 0000 0000
Number = - 0.75
= - 0.11two  20 (base 2 scientific notation)
= - 1.1two  2-1 (normalized scientific notation)
Sign: negative => 1
Exponent:
  Bias adjustment: -1 +127 = 126
  126ten = 0111 1110two

## Slide 94: Fraction Part: Decimal to Binary
0.75 x 2 = 1.5
0.5 x 2 = 1.0
0.11

## Slide 95: Example 2: Decimal to FP
A more difficult case: representing 1/3?
  = 0.33333…10 = 0.0101010101… 2  20 (base 2)
  = 1.0101010101… 2  2-2 (normalization)
  Sign: 0
  Exponent = -2 + 127 = 12510=011111012
  Significand = 0101010101…
0
0111 1101
0101 0101 0101 0101 0101 010

## Slide 96: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 10. 2 = 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38
95

## Slide 97: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 10. 2 = 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 98: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 99: Zero and Special Numbers
What have we defined so far? (single precision)
  Exponent Significand Object
  0 0 ???
  0 nonzero ???
  1-254 anything +/- floating-point
  255 0 ???
  255 nonzero ???

## Slide 100: Zero and Special Numbers
What have we defined so far? (single precision)
  Exponent Significand Object
  0 0 ???
  0 nonzero ???
  1-254 anything +/- floating-point
  255 0 ???
  255 nonzero ???
99

## Slide 101: Representation for 0
Represent 0?
  exponent all zeroes
  significand all zeroes too
  What about sign?
  +0: 0 00000000 00000000000000000000000
  -0: 1 00000000 00000000000000000000000

## Slide 102: Special Numbers
What have we defined so far? (single precision)
  Exponent Significand Object
  0 0 0
  0 nonzero ???
  1-254 anything +/- floating-point
  255 0 ???
  255 nonzero ???
Range:
  1.0  2-126  1.8  10-38 What if result too small? (>0, < 1.8x10-38 => Underflow!)
  (2 – 2-23)  2127  3.4  1038 What if result too large? (> 3.4x1038 => Overflow!)

## Slide 103: Gradual Underflow
Represent denormalized numbers (denorms)
  Exponent : all zeroes
  Significand : non-zeroes
  Allow a number to degrade in significance until it become 0 (gradual underflow)
102
0
0000 0000
0100 0000 0000 0000 0000 000
= 0.012  2-126

## Slide 104: Smallest Number
  The smallest normalized number
    1.0000 0000 0000 0000 0000 000  2-126
  The smallest de-normalized number
    0.0000 0000 0000 0000 0000 001  2-126
103

## Slide 105: Special Numbers
What have we defined so far? (single precision)
  Exponent Significand Object
  0 0 0
  0 nonzero denorm
  1-254 anything +/- floating-point
  255 0 ???
  255 nonzero ???

## Slide 106: Representation for +/- Infinity
In FP, divide by zero should produce +/- infinity, not overflow
Why?
  OK to do further computations with infinity, e.g., X/0 > Y may be a valid comparison
IEEE 754 represents +/- infinity
  Most positive exponent reserved for infinity
  Significands all zeroes
S
1111 1111
0000 0000 0000 0000 0000 000

## Slide 107: Special Numbers (cont’d)
What have we defined so far? (single-precision)
Exponent Significand Object
0 0 0
0 nonzero denom
1-254 anything +/- fl. pt. #
255 0 +/- infinity
255 nonzero ???

## Slide 108: Representation for Not a Number
What do I get if I calculate sqrt(-4.0) or 0/0?
  If infinity is not an error, these should not be either
  They are called Not a Number (NaN)
  Exponent = 255, Significand nonzero
Why is this useful?
  Hope NaNs help with debugging?
  They contaminate: op(NaN,X) = NaN
  OK if calculate but don’t use it

## Slide 109: Special Numbers (cont’d)
What have we defined so far? (single-precision)
Exponent Significand Object
0 0 0
0 nonzero denom
1-254 anything +/- fl. pt. #
255 0 +/- infinity
255 nonzero NaN

## Slide 110: Outline
Addition and subtraction
Constructing an arithmetic logic unit
  Building ALU
    Add, sub, and, or, nor
    Set-on-less-than, overflow detection, zero detection
  Fast adders
    Cascaded carry lookahead adder
    Multiple level carry lookahead adder
Multiplication
  Unsigned multiply
  Signed multiply
Division
Floating point
  Representations
  Addition and multiplication
109

## Slide 111: Floating-Point Addition
Basic addition algorithm:
(1) Align binary point :compute Ye – Xe
  right shift the smaller number, say Xm, that many positions to form Xm  2Xe-Ye
(2) Add mantissa: compute Xm  2Xe-Ye + Ym
(3) Normalization & check for over/underflow if necessary:
  left shift result, decrement result exponent
  right shift result, increment result exponent
  check overflow or underflow during the shift
(4) Round the mantissa and renormalize if necessary

## Slide 112: Floating-Point Addition Example
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add mantissa
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625

## Slide 113
Step 1
Step 2
Step 3
Step 4

## Slide 114: FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 115: Floating-Point Multiplication
Arithmetic-114
Basic multiplication algorithm
(1) Add exponents of operands to get exponent of product
doubly biased exponent must be corrected:
Xe = 7
Ye = -3
Excess 8
=4+8 = 12 = 01100
need extra subtraction step of the bias amount
(2) Multiplication of operand mantissa
(3) Normalize the product & check overflow or underflow during the shift
(4) Round the mantissa and renormalize if necessary
(5) Set the sign of product
Xe = 1111
Ye = 0101
10100
= 15
= 5
= 20
= 7 + 8
= -3 + 8
= 4 + 8 + 8

## Slide 116: Floating-Point Multiplication Example
Now consider a 4-digit binary example
  1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)
1. Add exponents
  Unbiased: –1 + –2 = –3
  Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127
2. Multiply operand mantissa
  1.0002 × 1.1102 = 1.1102  1.1102 × 2–3
3. Normalize result & check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4. Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5. Determine sign:
  –1.1102 × 2–3 = –0.21875

## Slide 117: MIPS R2000 Organization
116

## Slide 118: MIPS Floating Point
Separate floating point instructions:
  Single precision: add.s,sub.s,mul.s,div.s
  Double precision: add.d,sub.d,mul.d,div.d
FP part of the processor:
  contains 32 32-bit registers: $f0, $f1, …
  most registers specified in .s and .d instruction refer to this set
  Double precision: by convention, even/odd pair contain one DP FP number: $f0/$f1, $f2/$f3
  separate load and store: lwc1 and swc1
  Instructions to move data between main processor and coprocessors:
    mfc0, mtc0, mfc1, mtc1, etc.
Notes: lwcz: lw means load word, c co-processor ( z= 0 traps processor, z=1 floating point unit)
Lwc1 : lw to floating point co-processor

## Slide 119: Interpretation of Data
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs
The BIG Picture

## Slide 120: Associativity
Therefore, Floating Point add, subtract are not associative!
  Why? FP result approximates real result!
  This example: 1.5 x 1038 is so much larger than 1.0 that 1.5 x 1038 + 1.0 in floating point representation is still 1.5 x 1038
Floating Point add, subtract associative ?

## Slide 121: Associativity in Parallel Programming
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
Need to validate parallel programs under varying degrees of parallelism

## Slide 122: Concluding Remarks
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to reals
Bounded range and precision
  Operations can overflow and underflow
MIPS ISA
  Core instructions: 54 most frequently used
    100% of SPECINT, 97% of SPECFP
  Other instructions: less frequent